## Slide 1: Asynchronous Serial Communications
Origins of Serial Communications
  Modems and Telephones, DTE/DCE equipment
Digital Serial Communications
  Simplex, half-duplex and full-duplex
  Asynchronous serial transmission
  The Motorola 6850 (ACIA)
The RS-232C Standard
  Mechanical and electrical specs
  Control lines
  Handshaking
  Null modem
©Paul Davies. Not to be copied, used, or revised without explicit written permission from the copyright owner.

## Slide 2: Origins of Serial Communications and RS232
Analog : Telephone Lines
Digital: RS232
1
1
0
1
1
0
1
1
0
1
1
0
Digital: RS232
DTE
(Data Terminal Equipment)
DTE
(Data Terminal Equipment)
DCE
(Data Communications Equipment)
DCE
(Data Communications Equipment)
Communications over the Telephone Line
DTE equipment lies at each end. It is the origin and destination of data. Typical DTE equipment today includes computers, printers terminals etc.
DCE equipment sits between DTE equipment and converts digital data into whatever form is required to transmit that data over the communications medium, e.g. telephone lines, fibre optic, wireless comms etc. A typical piece of DCE equipment is a MODEM or Modulator/demodulator
RS232 is a digital communications standard to link DTE to DCE equipment

## Slide 3: Serial Communications and the Internet
Analog : Telephone Lines
Digital: Ethernet
1
1
0
1
1
0
1
1
0
1
1
0
Digital: Ethernet
DTE
(Data Terminal Equipment)
DTE
(Data Terminal Equipment)
DCE
(Data Communications Equipment)
DCE
(Data Communications Equipment)
We use those origins today as the basis of the internet, with high speed modems linking computers around the world, however, the RS232 link has been superseded by Ethernet for massively increased speed.
RS232 has also been replaced by other forms of serial communications such as USB, Serial ATA (disk drives) and Firewire. Although faster, these are hugely more complex than RS232 from both a S/W and H/W perspective.
RS232 is still the choice for low speed easy to use communications.

## Slide 4: Serial Communications and the Internet
A few years ago, PCs were equipped with RS232 and Printer ports, but the size of the connectors and the limited applications for them (in the PC world) means that they are no longer fitted as standard.
However many small embedded computers and peripherals still have RS232 ports. You can use a USB/RS232 converter to allow RS232 communications via the PC’s USB ports.
USB to RS232 converter
DE2 board
RS232 Serial port on early PC motherboard
Parallel Printer port on early PC motherboard
USB Port
RS232 Port
USB Cable

## Slide 5: Asynchronous Serial Communications
RS-232 is a standard defined by the Electronic Industries Association ("EIA").
There are three flavours of RS-232 (A, B, and C) with each one defining a different voltage range. The most commonly used variety is RS-232C, which uses a voltage range of between -12V to -3V to represent logic 1’s and +3v to +12v to represent logic 0’s in the digital data stream.
RS-232C cable lengths are limited to about 25 feet (8m).
Computers use some kind of UART (Universal Asynchronous Receiver/Transmitter) to convert between parallel (byte wide) data and serial data e.g. the 6850 chip.
“Line driver” chips then convert the stream of digital 0s and 1’s coming from the UART into the voltage levels required by the RS232 standard before they emerge from a suitable connector.
NOTE: If you don’t want RS232 voltage levels you can just use the digital data stream directly from the UART this allows for a simple 3 wire 5 volt serial communications
CPU
UART
(6850)
Line Driver (MAX232)
Parallel Digital
Serial Digital
RS232C Voltage Levels -12v/+12v
Computer
9 pin connector

## Slide 6: Some Terminology used in Serial Transmission
Baud rate - is a measure of the switching speed of a signal, that is, the number of times per second that a signal changes state or transitions.
Bits per second (bps) – is a measure of the rate at which data can be transmitted. For example, a slow dial up modem may quote only 56K bps
Baud rate and bps do not always mean the same thing. A signal may transition ‘ten’ times per second i.e. it’s baud rate is ten, but if the signal’s amplitude has 4 distinct voltage levels then each transition can convey 2 bits of information, i.e. its bps is 20.
For digital serial comms: BPS = Baud Rate since the signal only transitions between two voltage levels. RS232 always refers to “baud rate” as a measure of BPS.
Industry Standard baud rates are: 110, 300, 600, 1200, 4800, 9600, 14400, 19200, 38400, and so on.
11
10
01
00
Data
Time
0 T 2T 3T 4T 5T 6T 7T
Voltage

## Slide 7: Modes of Communications
Regardless of how the communication is implemented (e.g. serial, parallel, cable, fibre optic etc.), when two pieces of equipment are connected together, we have a choice about the way in which they are able to communicate.
Simplex Communication (Uni-directional)
  With a simplex connection, data can only flow in one direction, in much the same way that traffic is allowed to travel down a one-way street.
  An example of simplex communication is the television or radio.
  Simplex channels are rarely used in computer based systems because it is not possible for the receiver to send back any error, control or acknowledge signals to the sender.
Simplex (1 way data)
Sender
Receiver

## Slide 8: Modes of Communications
Half Duplex Communications (Bi-directional)
  A half duplex connection can send and receive, but not at the same time. It’s like a one-lane bridge where two way traffic must give way in order to cross.
  For bi-directional communications, each end has to reconfigure itself for transmitting or receiving. Computer controlled electronic switches are employed within each piece of equipment to dynamically switch data direction.
  As with the bridge, a problem of synchronisation always exists, i.e. who speaks first. Usually there is a master/slave relationship. The master (e.g. computer) controls all communication and the slave only speaks when spoken to (e.g. disk drive).
  An example of a Half-duplex communication system might be a walkie-talkie, with a separate speak/listen button. USB and ethernet uses half duplex communications because it results in fewer wires.
Half Duplex (2 Way) but not at the same time
Sender/Receiver
Sender/Receiver
Switches
Switches
Out
In
Out
In

## Slide 9: Modes of Communications
Full Duplex Communications (Bi-directional)
  Data can travel in both directions simultaneously.
  There is no need to switch between transmit and receive modes.
  Its like a two lane bridge or a two-lane highway.
  This type of communication requires only 3 wires, a ground, a transmit and a receive signal.
  Fire wire and RS-232 use full duplex communications as well as simple digital serial comms.
Full Duplex (2 Way)
Sender/Receiver
Sender/Receiver
Out
In
In
Out

## Slide 10: Universal Asynchronous Receiver/Transmitter(UART)
Most UARTS are full duplex
  They have separate pins and electronic hardware for the transmitter and receiver sections of the device that allows serial output and serial input to take place at the same time.
Operation is based around shift registers and a clock signal.
A UART clock (often referred to as the baud rate generator) determines shift register speed and hence data rate (bps)
Most UARTs can also generate parity bits for transmission and perform parity checking on reception to provide simple error detection.

## Slide 11: UART - Transmitter
Transmitter (Tx) - converts parallel data to serial data
  Inserts start and stop bits used to indicate start and end of transmission.
  Calculates and inserts parity bit if required into transmission.
  Data rate is determined by the UART transmitter clock.
Serial output
Parallel data written by Computer
Transmitter Clock - from a baud rate generator circuit
Status information back to computer (e.g. ready or error etc.)
UART
0’s and 1’s
time
0-5v digital signal

## Slide 12: RS232 Data Transmission and Framing
When no data is being transmitted, the RS232 transmit signal remains at the IDLE (or Mark) level – Logical 1 (but actually -12v).
Before a character can be transmitted it must first be ‘framed’. The format of a typical character frame is as follows:-
  A Start bit: logical 0 (also called a space +12v) indicates the start of a character.
  7 or 8 Data bits
  An Optional Odd/Even/No Parity bit used for possible error checking.
  1 or 2 Stop bits at logical 1 (called a mark) that is used to indicate the end of the transmission of that item of data. (Two stop bits were used with old teletypes to give the mechanicals the opportunity to recover and prepare for the next characters. These days, 1 stop bit is common).
Mark
Space
Start Bit
Optional Parity Bit
7 or 8 Data Bits
1 or 2 Stop Bits
1 Item of Data
T

## Slide 13: RS232 Data Transmission and Framing
Given these combinations, there are 12 possible formats for a character frame. Both transmitter and receiver have to agree the format.
The illustration here shows how the letter ‘M’ would be framed and transmitted. Notice how the least significant bit is transmitted first, i.e. little Endian.
As you can see, Asynchronous transmission is highly inefficient since with 8 data bits, a single start, stop and parity bit, we have only 73% data efficiency
Mark
(Idle)
Space
Start
Letter M = ASCII $4D = 010011012 (even Parity = 0)
1
0
1
1
0
0
1
0
Stop
-12v
+12v
Time
0

## Slide 14: Problem
Exercise
Draw the RS-232 bit pattern when transmitting the last three digits of your student number in ASCII.
Assume the serial port is configured as 8-bits, 1 stop bit, even parity.
How long does it takes to transmit these three digits at a clock speed to 9600 hz?
Character | ASCII
0 | $30
1 | $31
2 | $32
3 | $33
4 | $34
5 | $35
6 | $36
7 | $37
8 | $38
9 | $39

## Slide 15: Solution
S 1 1 1 0 1 1 0 0 p s S 1 0 0 1 1 1 0 0 p s S 0 1 0 0 1 1 0 0 p s
‘7’=00110111
‘9’=00111001
‘2’=00110010
Five ‘1s’ in character, so parity bit set to 1.
Four ‘1s’ in character, so parity bit set to 0.
Three ‘1s’ in character, so parity bit set to 1.
It takes 3*11*(1/9600)=3.4375ms to transmit the three digits.

## Slide 16: UART - Receiver
Receiver (Rx) Converts Serial Format Data back to Parallel
  Rx synchronises to transmitter using the start bit.
  Calculates parity and checks against received parity bit.
Receiver Clock - from a baud rate generator circuit
UART
Serial input
Parallel data read by Computer
Status information back to computer (e.g. ready or error etc.)
time
0-5v digital signal

## Slide 17: Synchronising Receiver to Incoming Data
How is data reception guaranteed, given that RS-232 does not contain a clock that sender and receiver can synchronise too?
Receiver samples the incoming data stream 16x’s faster than data (bit) rate.
As soon as the start bit is identified, receiver synchronises it’s shift register to the middle of 1st data bit time period, (i.e. 8 clock periods after detection of start bit.) and thereafter samples each data bit every 16 clock periods.
This means sender and receiver clocks can differ by as much as 2% (easily achieved using crystal oscillators) and still not drift to the point where the wrong data is sampled.
Waiting for start bit
Start bit
1st data bit = 1
Start Bit detected
Idle
Data Stream Sampled Here
Data Stream Sampled Here
2nd data bit = 0
Receiver Clock Synchronised Here
8 clocks
16 clocks
16 clocks

## Slide 18: Exercises
Homework
The bit stream below shows a RS-232 message transmitted with 7 data bits, odd parity, and 2 stop bits.
Decipher the message assuming the characters transmitted are ASCII.
Remember least significant bits transmitted first.
S0001001Ps S0110001Ps S0011001Ps S000010Ps
1000110 = $46 = F
1001000 = $48 = H
100000 = $40 = @
1001100 = $4C = L

## Slide 19: The Motorola 6850 ACIA (UART)
Introduction, History and External Interface
The Motorola 6850 ACIA (a kind of UART) was one of the first single chip devices to handle the burden of asynchronous serial data.
It has been rewritten in VHDL and is available on OpenCores.org.
Address A31-0
Clock

## Slide 20: The Motorola 6850 ACIA
6850 Internal Architecture - 4 byte wide Registers:
Control + Status at address hex 00400040
Transmit + Receive Data at address hex 00400042

## Slide 21: The Motorola 6850 ACIA
The 6850 Control Register (write only)
Bits 0-1: Reset and Clock divisor
  Provide a software master reset for the device.
  Clock division ratio (1, 16 or 64) for the transmitter and receiver.
Bits2-4: Frame Format
  Data width (7 or 8 bits),
  Parity (odd, even, none),
  Number of stop bits (1 or 2).
Bits 5-6: Transmitter Control
  The RTS line used with a modem.
  Whether the transmitter should generate an interrupt when the last character has been sent.
Bit 7 : Receiver Control
  Determines whether the 6850 should generate an interrupt when a character is received.

## Slide 22: The Motorola 6850 ACIA
The 6850 Status Register (Read only)
Bits 0,1 (RDRF, TDRE)
  Bit 0 set to logic 1, if the receive data register is holding an unread character.
  Bit 1 set to logic 1 when the transmit data register is empty.
  Polling algorithms can check the status of these bits to determine if new characters have been received or previous ones transmitted.
  Bit 0 is cleared when the receive data register is read from
  Bit 1 is cleared when the transmit data register is written to.
Bit 2 (DCD)
  This bit reflects the status of the hardware modem control signal ‘Data Carrier Detect’ (DCD). It is used to inhibit reception of data unless an associated modem has detected a carrier signal.
Bit 3 (CTS)
  This bit reflects the status of the hardware modem control signal ‘Clear to Send’. An active low signal on the 6850 CTS line indicates that some connected device is ready to receive more data from the 6850. This is a handshake signal in effect saying to the 6850 that it is clear to transmit more data.

## Slide 23: The Motorola 6850 ACIA
Bit 4 (FE)
  This bit is set whenever the 6850 detects that a received character is incorrectly framed. Examples include reception of a character with the incorrect number of stop bits. This bit is set/cleared on a character by character basis.
Bit 5 (OVRN)
  This bit indicates that the 6850 has been overrun by received characters that were not read by the CPU. The implication being that data has been lost. This bit is set/cleared on a character by character basis.
Bit 6 (PE)
  This bit is set whenever the 6850 detects that a received character has Incorrect Parity. This bit is set/cleared on a character by character basis.
Bit 7 (IRQ)
  This bit is set whenever the 6850 wishes to interrupt the CPU. Typically this occurs when transmit buffer empty or receive buffer full interrupts have been enabled in the control register and is also set when Bit 2 (DCD) is set

## Slide 24: The Baud Rate Generator
BR Generator
Xtal Osc
Address A31-0
Clock
Baud Rate Generator
Xtal Osc
Programmable Baud Rate Generator at address. Write to this address to set baud rate.
  001 = 115k baud
  010 = 57.6k baud
  011 = 38.4k baud
  100 = 19.2 baud
  all others = 9600 baud

## Slide 25: The Motorola 6850 ACIA
68000 Assembly Language Routines to Initialise 6850 (addresses are just examples)
ACIAControl equ $00400040
ACIAStatus equ $00400040
ACIATransmit equ $00400042
ACIAReceive equ $00400042
BaudRateGen equ $00400044
***********************************************************************************************
* Initialise 6850 and baud rate generator for 115k Baud
* clock (16x), no RX/TX interrupts, RTS set low, 8 bit data, no parity, 1 stop bit
* All registers preserved
***********************************************************************************************
Initialise move.b #%00000001, BaudRateGen ; Program Baud rate for 115k
move.b #%00000011, ACIAControl ; reset ACIA
move.b #%00010101, ACIAControl ; x16 clock, 8 data, no parity, 1 stop, no interrupt
rts

## Slide 26: The Motorola 6850 ACIA
68000 Assembly Language routines to Poll for character received
Control equ $00400040
Status equ $00400040
Transmit equ $00400042
Receive equ $00400042
DataRateGen equ $00400044
***********************************************************************************************
* Read status register until bit 0 = 1, then read receive data register and
* return character in d0.b. All other registers preserved
***********************************************************************************************
Getchar move.b Status,d0 ; read status register into d0
and.b #%00000001,d0 ; mask off bits 7-1, leaving bit 0
cmp.b #%00000001,d0 ; is bit 0 = 1?
bne Getchar ; if not keep polling
move.b Receive,d0 ; read received character into d0
rts

## Slide 27: The Motorola 6850 ACIA
68000 Assembly Language routines to Poll status prior to Transmitting
Control equ $00400040
Status equ $00400040
Transmit equ $00400042
Receive equ $00400042
DataRateGen equ $00400044
***********************************************************************************************
* Transmit Data
* Character to transmit is in d0.b, all registers preserved
***********************************************************************************************
Putchar move.b d0,-(a7) ; push d0 into stack (save its value somewhere)
TxLoop move.b Status,d0 ; read status register into d0
and.b #%00000010,d0 ; mask off bits 7-2 and 0, leaving bit 1
cmp.b #%00000010,d0 ; is bit 1 = 1?
bne TxLoop ; if not keep polling
move.b (a7)+,d0 ; get character to transmit back off stack
move.b d0,Transmit ; write character to transmit register for transmission
rts

## Slide 28: The RS232 Standard
The RS- 232 (Recommended Standard - 232) was initially published in the 60’s.
Currently the standard has been ‘hacked about’ probably more than any other standard in existence for use way beyond its original applications, such as computer-to-computer or computer-to-printer applications.
More time has been spent by Engineers attempting to make computer equipment communicate on RS-232 than just about anything else in existence !!!
It has become so tricky connecting incompatible equipment together that ‘breakout’ boxes are now sold so that technicians can play around with connecting one signal to another and observe the state of each signal on LEDs in order to establish communications (see illustration)
RS232 “Break-out” Box

## Slide 29: The RS232 Standard
The RS232 Standard defines the following
  A Mechanical Specification
  A Protocol to control the transmission of data using handshaking
  An Electrical Specification

## Slide 30: The RS232 Mechanical Standard
The standard specifies that equipment be connected via a 25 pin D-Type connector (DB-25), although a 9 pin connector (DB-9) is more often employed these days for its associated space and cost savings.
The Female connector is generally (but not always) associated with DCE equipment (e.g. Modems, Printers, Terminals) while the Male connector is generally present on DTE equipment (computers etc.)

## Slide 31: The RS232 Protocol for Information Exchange
Request To Send (RTS), Pin 4
  Asserted by the computer to inform the modem that it wants to transmit data.
Clear To Send (CTS), Pin 5
  Asserted by the modem after receiving a RTS signal, indicating that the computer can now transmit.
Data Terminal Ready (DTR), Pin 20 (DB25) or Pin 4 (DB9)
  This signal is asserted by the computer, to inform the modem that the computer is ready to communicate
Data Set Ready (DSR), Pin 6
  This signal is asserted by the modem in response to a DTR signal from the computer and indicates the modem is ready to communicate.
Data Carrier Detect (DCD), Pin 8
  This signal is asserted by the modem, informing the computer that it has established a physical connection with the telephone network.
Transmit Data (TD), Pin 2
  This signal carries the transmitted data from the computer to the modem.
Receive Data (RD), Pin 3
  The signal carries the received data from the modem to the computer.
Status Signals
Data Signals
Control Flow Signals (Handshaking)

## Slide 32: RS-232 Handshaking
Handshaking
Handshaking is a protocol whereby if the receiver cannot keep up with the data rate of the sender, the receiver can slow down the sender.
There are two methods of handshaking. Most equipment supports both and is purely down to configuration or choice as to which to support
  Hardware: Using wires (RTS/CTS).
  Software: XON, XOFF

## Slide 33: RS-232 Handshaking
RTS/CTS Handshaking
If the sender is transmitting data too fast for the receiver to keep up, i.e. the receivers data buffers are getting full and it cannot process that amount of data so quickly, it will remove the CTS (Clear-to-send) signal, this will disable the sender from transmitting.
The 6850s transmitter section is hard wired to this signal so it will not transmit unless CTS (Clear-to-send) signal is active.
Note handshaking works only in one direction, that is, that DCE equipment (e.g. modem, printer, terminal etc.) is slow and thus needs to can control the transmission speed of DTE equipment, e.g. computer.
It is assumed that a computer (DTE) is fast enough to keep up with any minimal data back from say a printer, terminal or Modem (DCE). Two computers should be fast enough to keep up with each (given that physical communications over the RS232 is quite slow). However, Xon-Xoff can be used if they need to control each other

## Slide 34: RS-232 Handshaking
TXD
RXD
CTS
RTS
DSR
DTR
DCD
GND
TXD
RXD
CTS
RTS
DSR
DTR
DCD
GND
Computer (DTE)
Modem (DCE)
Configuration for Hardware Handshaking, e.g. Computer to Modem
Request to Send
Clear to Send
Transmitting
Too Fast !!!
That’s Better !!!
Ready
Ready
Phone line ready

## Slide 35: RS-232 Handshaking
Soft Handshaking using XON-XOFF
  In systems requiring the minimum of cabling complexity and cost, computers and peripherals can be connected without physical/electrical handshaking, that is CTS/RTS handshaking is disabled (or bypassed).
  Instead, a software protocol (as opposed to an electrical/signalling protocol) is employed whereby two way handshaking is implemented using the transmission of characters XON (free to transmit) and XOFF (stop transmitting).
  These characters correspond to hex 11 (Ctrl-Q) and hex 13 (Ctrl-S) from the ASCII chart.
  This protocol is not defined by the RS-232 standard but is more commonly used than CTS/RTS signalling, particularly when implementing Computer-to-Computer communications.
  In such situations, the CTS/RTS and DTR/DSR pins have to be wired together to permanently enable the communication devices.
  The illustration here demonstrates the idea when using a 3 wire cable to connect DTE/DTE equipment.

## Slide 36: RS-232 Software Handshaking
TXD
RXD
CTS
RTS
DSR
DTR
DCD
GND
TXD
RXD
CTS
RTS
DSR
DTR
DCD
GND
Computer (DTE)
Computer (DTE)
Configuration for Software Handshaking using minimal 3 wire connection Tx, Rx and ground, e.g. Computer to Computer (Note crossed over transmit and receive and CTS connected to RTS etc.)
Xoff
Xon
Too Fast !!!
Transmitting
That’s Better !!!

## Slide 37: The RS232 Electrical Standard
RS232 Electrical Interface
All Signals are valid in the range ±3 volts to ±25 volts although ±12v is more common. Signals within the range -3 volts to +3 volts are considered invalid.
MAX do a full range of RS-232 driver chips in various configurations. As do Linear Technologies, these convert digital (TTL voltage levels in he range 0-5 into RS-232 levels in the range ±12v.
Both sets of chips use on-chip circuitry to generate RS-232 voltage levels from a single 5v supply.
The example below uses Linear Technologies LT1080 chip.
6850

## Slide 38: DTE to DTE connections and Null Modems
RS-232C interface designed originally to connect computers to modems
However, many of today’s RS-232C applications are for connecting a computer (DTE) to either another computer or to a peripheral such as a printer (also considered a DTE), rather than to a modem (DCE)
In order to connect a computer to a computer (i.e. DTE to a DTE) we must cross over some of the control signals. This is where a break-out box can be useful !!
This DTE-DTE interface is accomplished with a special connector cable called a null modem
  A NULL modem simulates a DTE-DCE/DCE-DTE circuit
  A NULL modem has a female connector on both ends.
  The signals are wired as indicated in the figure overleaf.

## Slide 39: DTE to DTE connections and Null Modems
NULL Modem Connections for Computer to Computer Communication
Note how everything is crossed over
Handshaking Can be implemented using RTS/CTS or Xon-Xoff.
TXD
RXD
CTS
RTS
DSR
DTR
DCD
GND
TXD
RXD
CTS
RTS
DSR
DTR
DCD
GND
Computer (DTE)
Computer (DTE)
NULL Modem